## Slide 1: Computer Vision – Module 2
Dr. Sreejith Rajan

## Slide 2: Image Enhancement - Overview
Image enhancement improves visual quality or prepares image for further processing.
Enhancement includes:
  Contrast enhancement
  Intensity normalization
  Smoothing
  Noise removal
Important:
👉 Enhancement improves perception 👉 It does NOT add new information

## Slide 3: Contrast Enhancement
If intensity values lie in a narrow range → image looks dull.
We stretch values to full range 0–255.
Mathematical Model
Linear transformation.

## Slide 4
Characteristics
✔ Global operation ✔ Preserves relative brightness ✔ Does NOT remove noise ✔ Improves dynamic range
Applications
  X-ray image improvement
  Satellite images
  Underexposed images

## Slide 5: Contrast Normalisation
Standardize intensity of the image (Mostly for ML)
Formula
Characteristics
✔ Mean = 0 ✔ Variance = 1 ✔ Used before CNN input ✔ Produces negative values

## Slide 6
mean = average intensity of all 65,536 pixels
std = spread of intensity values (contrast measure)

## Slide 7: Image Smoothing
Reduce high-frequency components (noise).
Noise = rapid pixel fluctuations.
Smoothing = Low-pass filtering.
Types of smoothing
  Mean filter
  Gaussian Filter
  Median Filter

## Slide 8: Mean Filter
1️⃣ Mean Filter
Kernel:
Characteristics:
✔ Simple ✔ Linear ✔ Blurs edges ✔ Reduces Gaussian noise

## Slide 9: Gaussian Filter
Formula:
Characteristics:
✔ Linear ✔ Better edge preservation ✔ Controlled by σ ✔ Used in Canny edge detection

## Slide 10: Median Filter
Unlike mean or Gaussian filters:
  It does NOT average values
  It sorts values in the neighborhood
  It picks the median
So it is a non-linear filter.
For a 3×3 window:
Where:
= input image
= filtered image
I,j (Neighbourhood )= surrounding pixels

## Slide 11
Applications
✔ Biomedical images ✔ Surveillance systems ✔ Faulty sensor correction ✔ Preprocessing before segmentation
Filter | Linear? | Good for Gaussian Noise | Good for Salt & Pepper | Edge Preservation
Mean | Yes | Moderate | Poor | Poor
Gaussian | Yes | Good | Poor | Moderate
Median | No | Moderate | Excellent | Excellent

## Slide 12: Rank Filters
Instead of median, choose kth element.
Min filter → erosion
Max filter → dilation

## Slide 13: Erosion and Dilation
They are morphological operations used to process shapes in images.
They work using a small matrix called a structuring element (kernel).
They are commonly applied to:
  Binary images
  Grayscale images
  Segmented objects
Effect
✔ Expands objects ✔ Fills small holes ✔ Connects nearby components ✔ Thickens boundaries

## Slide 14
DILATION
Dilation grows bright regions (white objects).
It expands object boundaries.
Mathematical Definition (Binary Image)
Simplified explanation:
If ANY pixel under the kernel is white → output pixel becomes white.
Original object → grows outward after dilation.

## Slide 15
EROSION
Erosion shrinks bright regions.
It removes boundary pixels.
✔ Shrinks objects ✔ Removes small noise ✔ Breaks thin connections ✔ Thins boundaries

## Slide 16
Mathematical Definition
Simplified explanation:
Only if ALL pixels under kernel are white → output pixel remains white.
Effect
✔ Shrinks objects ✔ Removes small noise ✔ Breaks thin connections ✔ Thins boundaries
Intuitive Explanation
Dilation = “Add pixels”
Erosion = “Remove pixels”

## Slide 17: 2D Fourier Transform (Image Frequency Analysis)
When we move from 1D signals to images, we move from time → space.
An image is a 2D signal:
)
The 2D Continuous Fourier Transform (2D-CFT) is:
What does it mean?
→ spatial domain
→ frequency domain
Low frequencies → smooth variations
High frequencies → edges & sharp details

## Slide 18
Image filtering
Compression
Pattern recognition
Biomedical imaging etc

## Slide 19: Discrete Fourier Transform(DFT)
Now in digital systems , signals are discrete.
For N samples:
Why DFT matters:
  Implementable in software
  Used in FFT algorithms
  Image processing
  Audio processing
  Embedded DSP

## Slide 20: 2D DFT(for images)

## Slide 21: Factors Affecting DoF
Aperture
Camera Subject Distance
Sensor Size

## Slide 22: Aperture
Aperture is the opening in the lens that lets light pass through to the sensor.
Think of it as a pupil for your lens. It dilates to let more light in, and contracts to restrict light when it is bright.

## Slide 23
Captured with a NIKON D800 and 24-70mm f/2.8 lens @ 24mm, ISO 200, 8/10s, f/22.0
Captured with a NIKON D500 and 17-55mm f/2.8 lens @ 22mm, ISO 200, 1/1600s, f/2.8

## Slide 24: Camera- Subject Distance
The shorter that distance, the smaller the depth of field.

## Slide 25: Telecentric Lens
Telecentric lenses are designed to have a constant magnification regardless of the object's distance or location in the field of view.
This attribute is ideal for many machine vision measurement applications, as measurements of an object's dimensions will be independent of where it is located.
In order to achieve a telecentric lens design, all of the chief rays (rays from an off-axis point that pass through the centre of the aperture stop) have to be parallel to the optical axis in either image space or object space, or both.

## Slide 26: Types of Telecentric Lenses
Thorlabs · Telecentric Lenses Tutorial

## Slide 27: Lens Aberrations
Lens aberrations are optical imperfections that prevent a lens from forming a perfect image of an object.
In short: rays don’t meet where theory says they should.
An ideal lens would:
  Bring all rays to a single point
  Produce sharp, undistorted, color-accurate images

## Slide 28: Classification of Lens Aberrations
Monochromatic aberrations (independent of wavelength)
Chromatic aberrations (due to wavelength dependence)

## Slide 29: Monochromatic Aberrations- Spherical Aberration
Caused by spherical lens surfaces
Marginal rays focus at a different point than paraxial rays
Effect:
  Blurred image even on the optical axis
Fix:
  Aspherical lenses
  Aperture stop reduction

## Slide 30: Coma
Off-axis aberration
Magnification varies with aperture height
Effect:
  point image becomes comet-shaped
  Absent on optical axis

## Slide 31: Astigmatism
Tangential and sagittal rays focus at different distances
Effect:
  image of a point becomes two orthogonal line foci
Key surfaces: tangential focus, sagittal focus

## Slide 32: Field Curvature (Petzval Curvature)
Image surface is curved
Center and edges cannot be focused simultaneously on a flat screen
Key visual cue:
  🌙 Curved image plane

## Slide 33: Distortion
Distortion occurs because lateral magnification varies with field height (distance of the object point from the optical axis).
In an ideal lens, magnification is constant across the field.
In a real lens, magnification changes for off-axis points.
Image shape changes, but sharpness remains
Types:
  Barrel distortion → image bulges outward
  Pincushion distortion → image pinches inward

## Slide 34: Chromatic Aberrations
Caused by wavelength-dependent refractive index
Different colours focus at different positions because: n = f(λ)
Types:
  Longitudinal (axial): Colours focus at different distances along the axis
  Lateral (transverse): Colours focus at different magnifications
Effect:
  Colour fringes (purple/green edges)
  Loss of contrast
Fix:
  Achromatic doublets
  Apochromatic lenses

## Slide 35: CCD Camera (Charge Coupled Device)
Incoming light generates charge packets in each pixel.
Charges are shifted across the chip (like a bucket brigade) to a single output amplifier.
Conversion to voltage happens outside the pixel array.

## Slide 36: CCD Working

## Slide 37: CCD
Key Characteristics
Very low noise
Excellent image uniformity
High dynamic range
Higher power consumption
Slower readout
More expensive manufacturing
Major Applications
Scientific imaging
Astronomy
High-end microscopy
Medical imaging (older systems)

## Slide 38: CMOS Cameras (Complementary Metal-Oxide Semiconductor)
Each pixel has its own amplifier and readout circuitry.
Signal is converted to voltage inside the pixel.
Pixels are read row by row.

## Slide 39: CMOS
Key Characteristics
Low power consumption
High speed
Low cost
On-chip processing possible
More noise (older CMOS; modern ones are excellent)
Rolling shutter artifacts (in many sensors)
Applications
Mobile phone cameras
Webcams
Surveillance cameras
Embedded vision (ESP32-CAM, Raspberry Pi Camera)

## Slide 40: CCD vs CMOS
Feature | CCD | CMOS
Noise | Very low | Low (modern CMOS)
Speed | Slower | Faster
Power | High | Low
Cost | High | Low
Integration | External ADC | On-chip ADC
Shutter | Global | Rolling / Global

## Slide 41: Colour Cameras
Image sensors are naturally monochrome
To capture color, we use color separation techniques.
Two main approaches:
  Single-chip colour cameras
  Three-chip (3-CCD / 3-CMOS) cameras
Micro lens
Filter
Sensor

## Slide 42: Single Chip Camera
A Bayer filter array is placed on top of the sensor.
Each pixel sees only one color:
  50% Green
  25% Red
  25% Blue
Missing colors are reconstructed using demosaicing algorithms.

## Slide 43: Single Chip Colour Camera
Key Characteristics
Compact
Low cost
Low power
Ideal for embedded systems
Lower colour accuracy
Reduced resolution per colour
Colour artifacts possible
Applications
Smartphones
Consumer cameras
Machine vision (cost-sensitive)
IoT & embedded cameras

## Slide 44: Three-Chip (3-CCD / 3-CMOS) Colour Cameras
Incoming light passes through a dichroic prism.
Light is split into:
  Red → Sensor 1
  Green → Sensor 2
  Blue → Sensor 3
Each sensor captures full resolution for its colour.

## Slide 45: CMOS
Key Characteristics
Excellent color accuracy
High resolution
No demosaicing artifacts
Superior image quality
Bulky
Expensive
Precise optical alignment needed
Applications
Broadcast cameras
Cinematography
High-end industrial inspection
Scientific imaging

## Slide 46: Camera Performance Parameters-Resolution
Number of pixels in the image (Width × Height).
Example:
  640 × 480 (VGA)
  1920 × 1080 (Full HD)
  4K (3840 × 2160)
Key Points:
  Higher resolution → more detail
  Larger storage
  Higher processing load
  More memory usage

## Slide 47: Sensitivity(ISO)
Ability of camera sensor to capture light.
Measured in:
  ISO number
  Lux rating
  Responsivity (A/W in scientific sensors)
  Important: High sensitivity → works in low light But may increase noise

## Slide 48: Signal to Noise Ratio
Ratio of useful signal to unwanted noise.

## Slide 49: Dynamic Range
Ability to capture both dark and bright regions simultaneously.
Measured in:
  Stops (photography)
  dB (scientific systems)
High dynamic range (HDR) is important in:
  Microscopy
  Outdoor imaging
  Industrial inspection
Dynamic Range= Minimum Detectable Signal/Maximum Detectable Signal​
Often expressed in:
  dB (decibels)

## Slide 50: Example

## Slide 51: Frame Rate(FPS)
Number of frames captured per second.
Examples:
  30 FPS → normal video
  60 FPS → smooth motion
  120+ FPS → slow motion
In robotics or pick-and-place systems:
  High FPS → better real-time control

## Slide 52: Pixel Size
Larger pixel:
  More light captured
  Better low-light performance
  Better SNR
Smaller pixel:
  Higher resolution
  But less light per pixel
Trade-off between:
  Resolution vs Sensitivity

## Slide 53: Field of View(FOV)
Area covered by the camera lens.
Wide FOV:
  Surveillance
  Robotics navigation
Narrow FOV:
  Microscopy
  Precision inspection

## Slide 54: Latency
Time between image capture and output availability.
Critical for:
  Robotics
  Autonomous systems
  Real-time control

## Slide 55: Bit depth
Number of intensity levels per pixel.
  8-bit → 256 levels
  10-bit → 1024 levels
  12-bit → 4096 levels
  16-bit → 65536 levels
Higher bit depth:
  Better quantitative analysis
  Essential for medical imaging

## Slide 56: Dark Current
Important in scientific cameras.
Even in complete darkness, some electrons are generated.
More dark current:
  More noise
  Reduced accuracy
Critical in:
  Fluorescence imaging
  Long exposure microscopy

## Slide 57: Quantum Efficiency
Percentage of photons converted into electrons.
Higher QE → Better sensitivity.

## Slide 58: Noises In Camera –Shot Noise
Cause: Random arrival of photons
Nature: Statistical (Poisson distributed)
Increases with signal
Cannot be eliminated (fundamental physical limit)
Very important in:
  Fluorescence imaging
  Microscopy
  Low-light imaging

## Slide 59: Thermal Noise
Generated due to thermal electrons even when no light is present.
✔ Increases with temperature ✔ Reduced using cooling (scientific CCD/CMOS)

## Slide 60: Read Noise
Noise introduced during:
  Charge-to-voltage conversion
  Analog-to-digital conversion
  Independent of light intensity.
Dominant in:
  Low signal conditions
  Fast readout systems

## Slide 61: Fixed Pattern Noise
Caused by:
  Pixel-to-pixel variation
  Manufacturing mismatch
Appears as:
  Vertical stripes
  Grid patterns
Reduced using:
  Calibration
  Dark frame subtraction

## Slide 62: Quantisation Noise
Occurs due to limited bit depth during ADC.
Example:
  8-bit → only 256 intensity levels
  12-bit → 4096 levels
Lower bit depth → higher quantization error.

## Slide 63: Camera-Computer Interface
Camera-computer interfaces define how digital video data is transferred from a camera sensor to a processing system.
Digital Video Signal
  After image capture, the sensor produces digital signals containing:
• Pixel intensity values • Synchronization signals • Clock signals • Control signal

## Slide 64: Components of Digital Video Signal
Pixel Data (Parallel/Serial)
Clock Signal
Horizontal Sync (HSYNC)
Vertical Sync (VSYNC)
Frame Valid / Line Valid signals

## Slide 65: Specialised Interfaces
For example:
8-bit grayscale → 8 data lines
24-bit RGB → 24 data lines
High-resolution cameras produce extremely large data rates:
Example: 1920 × 1080 × 60 fps × 8 bits ≈ 995 Mbps
That’s why specialized interfaces are needed.

## Slide 66: Camera Link
Developed by Automated Imaging Association for industrial vision systems.

## Slide 67
Uses:
LVDS (Low Voltage Differential Signaling)
Parallel high-speed transmission
Requires frame grabber card in PC
Mode | Max Data Rate
Base | 255 MB/s
Medium | 510 MB/s
Full | 680 MB/s

## Slide 68
Advantages:
✔ Very reliable ✔ Low latency ✔ High bandwidth ✔ Industrial grade
Disadvantages:
✖ Expensive ✖ Requires frame grabber ✖ Short cable length
Used in:
Industrial inspection
Robotics
High-speed imaging

## Slide 69: IEEE 1394 (FireWire)
Developed by Apple

## Slide 70
Features
✔ Plug and play ✔ Isochronous transmission (real-time video) ✔ Direct memory access
Limitations:
✖ Becoming obsolete ✖ Limited bandwidth compared to modern standards
Used widely in:
Early machine vision systems
Scientific cameras
Video camcorders
Version | Speed
1394a (FireWire 400) | 400 Mbps
1394b (FireWire 800) | 800 Mbps

## Slide 71: USB 2.0(Universal Serial Bus)
Speed:480 Mbps (theoretical max)
Features:
✔ Very cheap ✔ No frame grabber required ✔ Plug-and-play ✔ Widely supported
Limitations:
✖ CPU-dependent ✖ Not ideal for very high-speed cameras ✖ Limited cable length (~5m)
Used in:
Webcams
Low-cost vision systems
Embedded imaging

## Slide 72: Comparison
Feature | Camera Link | IEEE 1394 | USB 2.0
Type | Industrial | Serial bus | Universal bus
Max Speed | 680 MB/s | 800 Mbps | 480 Mbps
Frame Grabber | Required | Not required | Not required
Cost | High | Medium | Low
Usage | Industrial vision | Scientific | Consumer