## Slide 1: Computer Vision – Module 1
Dr. Sreejith Rajan

## Slide 2: Course Objectives
To understand the fundamentals of image processing
To familiarise with image enhancement and image segmentation algorithms
To familiarise with computer vision concepts
Comprehensive understanding of feature extraction and image matching techniques.

## Slide 3: Pinhole Camera
A pinhole camera is a simple optical device that uses a tiny aperture to project an inverted image of an external scene onto a surface inside a light-tight box.
It works on the principle of rectilinear motion of light.
Image will be real, inverted and diminished
Role of Pinhole size on image?
  Small pinhole
  Large pinhole

## Slide 4: Characteristics of Pinhole Camera
No lens required
Infinite depth of field
No focusing mechanism
Very low light efficiency
Simple construction

## Slide 5: Advantages of Pinhole Camera
No lens aberrations
Very large depth of field
Easy to understand and build
Used as a basic imaging model

## Slide 6: Limitations of Pinhole Camera
Low brightness
Poor resolution compared to a lens-based camera
Not suitable for low light conditions

## Slide 7: Fundamentals of Gaussian Optics
Gaussian optics is based on the principles of ray optics.
A point source of light emits light rays in all directions.
Light rays propagate in straight lines in a homogeneous medium.
Light rays from a distant source are considered parallel.
Spherical lenses and spherical mirrors obey Gaussian optics when only paraxial rays are considered.
For rays close to the principal axis, the small-angle approximation is valid, leading to simple image-formation equations.

## Slide 8: Paraxial Approximation
The paraxial approximation assumes that light rays make small angles with the principal (optical) axis.
Under this condition:
  sin⁡𝜃≈tan⁡𝜃≈𝜃(𝜃 in radians)
This approximation simplifies the geometry of light propagation and leads to linear image-formation equations.
The paraxial approximation is the foundation of Gaussian optics and is valid only for rays close to the optical axis.

## Slide 9: Image Formation in Spherical Mirrors/Lenses

## Slide 10: Gaussian Optics for Spherical Mirrors
Concave and Convex mirrors are the simplest examples of spherical mirrors.
Spherical mirrors can be considered as many tiny plane mirrors placed side by side.
A normal is drawn along the radius of curvature
Reflection happens with respect to this normal

## Slide 11: Concave Mirror
Incident ray strikes the mirror at point P.
Normal is drawn through the centre of curvature (C).
Reflected ray makes an equal angle with the normal.
Multiple reflected rays converge to the focus.
Golden rule for mirrors: Angle of incidence(i) = Angle of
Reflection (r)

## Slide 12: Convex Mirror
Incident ray hits curved surface
Normal again passes through centre of curvature
Reflection obeys 𝑖=𝑟
Reflected rays diverge
Extensions meet at a virtual focus behind mirror

## Slide 13: Mirror Equations
= +
=focal length
= image distance from pole
= object distance from pole
Magnification,
Spcial Relation : , where R =Radius of curvature of the mirror

## Slide 14: Spherical Lenses
Lenses Obey Snell’s law of refraction
n1sin i=n2sinr
This applies at each refracting surface of the lens.
Why lenses bend light
  Light enters glass → slows down → bends towards normal
  Light exits glass → speeds up → bends away from normal
  Net result: convergence or divergence

## Slide 15: Convex lens
Ray enters lens from air to glass → refracts towards normal
Ray exits glass to air → refracts away from normal
Due to curved surfaces, rays converge
Rays meet at the real focus on the opposite side

## Slide 16: Concave Lens
Refraction at first surface causes divergence
Second refraction increases divergence
Rays appear to come from a virtual focus
Image is always virtual and diminished

## Slide 17: Lens Equations
= -
=focal length
= image distance from pole
= object distance from pole
Magnification

## Slide 18: Lens vs Mirror
Aspect | Mirrors | Lenses
Physical process | Reflection | Refraction
Governing law | ( i = r ) | Snell’s law
Medium change | No | Yes
Image formation | Single interaction | Two refractions
Gaussian optics role | Geometry | Approximation

## Slide 19: Depth of Field
Depth of field is the distance between the closest and farthest objects in a photo that appears acceptably sharp.
Now your camera can only focus sharply at one point. But the transition from sharp to unsharp is gradual, and the term ‘acceptably sharp’ is a loose one
Credits : Elizabeth
https://photographylife.com/what-is-depth-of-field

## Slide 20: Factors Affecting DoF
Aperture
Camera Subject Distance
Sensor Size

## Slide 21: Aperture
Aperture is the opening in the lens that lets light pass through to the sensor.
Think of it as a pupil for your lens. It dilates to let more light in, and contracts to restrict light when it is bright.

## Slide 22
Captured with a NIKON D800 and 24-70mm f/2.8 lens @ 24mm, ISO 200, 8/10s, f/22.0
Captured with a NIKON D500 and 17-55mm f/2.8 lens @ 22mm, ISO 200, 1/1600s, f/2.8

## Slide 23: Camera- Subject Distance
The shorter that distance, the smaller the depth of field.

## Slide 24: Telecentric Lens
Telecentric lenses are designed to have a constant magnification regardless of the object's distance or location in the field of view.
This attribute is ideal for many machine vision measurement applications, as measurements of an object's dimensions will be independent of where it is located.
In order to achieve a telecentric lens design, all of the chief rays (rays from an off-axis point that pass through the centre of the aperture stop) have to be parallel to the optical axis in either image space or object space, or both.

## Slide 25: Types of Telecentric Lenses
Thorlabs · Telecentric Lenses Tutorial

## Slide 26: Lens Aberrations
Lens aberrations are optical imperfections that prevent a lens from forming a perfect image of an object.
In short: rays don’t meet where theory says they should.
An ideal lens would:
  Bring all rays to a single point
  Produce sharp, undistorted, color-accurate images

## Slide 27: Classification of Lens Aberrations
Monochromatic aberrations (independent of wavelength)
Chromatic aberrations (due to wavelength dependence)

## Slide 28: Monochromatic Aberrations- Spherical Aberration
Caused by spherical lens surfaces
Marginal rays focus at a different point than paraxial rays
Effect:
  Blurred image even on the optical axis
Fix:
  Aspherical lenses
  Aperture stop reduction

## Slide 29: Coma
Off-axis aberration
Magnification varies with aperture height
Effect:
  point image becomes comet-shaped
  Absent on optical axis

## Slide 30: Astigmatism
Tangential and sagittal rays focus at different distances
Effect:
  image of a point becomes two orthogonal line foci
Key surfaces: tangential focus, sagittal focus

## Slide 31: Field Curvature (Petzval Curvature)
Image surface is curved
Center and edges cannot be focused simultaneously on a flat screen
Key visual cue:
  🌙 Curved image plane

## Slide 32: Distortion
Distortion occurs because lateral magnification varies with field height (distance of the object point from the optical axis).
In an ideal lens, magnification is constant across the field.
In a real lens, magnification changes for off-axis points.
Image shape changes, but sharpness remains
Types:
  Barrel distortion → image bulges outward
  Pincushion distortion → image pinches inward

## Slide 33: Chromatic Aberrations
Caused by wavelength-dependent refractive index
Different colours focus at different positions because: n = f(λ)
Types:
  Longitudinal (axial): Colours focus at different distances along the axis
  Lateral (transverse): Colours focus at different magnifications
Effect:
  Colour fringes (purple/green edges)
  Loss of contrast
Fix:
  Achromatic doublets
  Apochromatic lenses

## Slide 34: CCD Camera (Charge Coupled Device)
Incoming light generates charge packets in each pixel.
Charges are shifted across the chip (like a bucket brigade) to a single output amplifier.
Conversion to voltage happens outside the pixel array.

## Slide 35: CCD Working

## Slide 36: CCD
Key Characteristics
Very low noise
Excellent image uniformity
High dynamic range
Higher power consumption
Slower readout
More expensive manufacturing
Major Applications
Scientific imaging
Astronomy
High-end microscopy
Medical imaging (older systems)

## Slide 37: CMOS Cameras (Complementary Metal-Oxide Semiconductor)
Each pixel has its own amplifier and readout circuitry.
Signal is converted to voltage inside the pixel.
Pixels are read row by row.

## Slide 38: CMOS
Key Characteristics
Low power consumption
High speed
Low cost
On-chip processing possible
More noise (older CMOS; modern ones are excellent)
Rolling shutter artifacts (in many sensors)
Applications
Mobile phone cameras
Webcams
Surveillance cameras
Embedded vision (ESP32-CAM, Raspberry Pi Camera)

## Slide 39: CCD vs CMOS
Feature | CCD | CMOS
Noise | Very low | Low (modern CMOS)
Speed | Slower | Faster
Power | High | Low
Cost | High | Low
Integration | External ADC | On-chip ADC
Shutter | Global | Rolling / Global

## Slide 40: Colour Cameras
Image sensors are naturally monochrome
To capture color, we use color separation techniques.
Two main approaches:
  Single-chip colour cameras
  Three-chip (3-CCD / 3-CMOS) cameras
Micro lens
Filter
Sensor

## Slide 41: Single Chip Camera
A Bayer filter array is placed on top of the sensor.
Each pixel sees only one color:
  50% Green
  25% Red
  25% Blue
Missing colors are reconstructed using demosaicing algorithms.

## Slide 42: Single Chip Colour Camera
Key Characteristics
Compact
Low cost
Low power
Ideal for embedded systems
Lower colour accuracy
Reduced resolution per colour
Colour artifacts possible
Applications
Smartphones
Consumer cameras
Machine vision (cost-sensitive)
IoT & embedded cameras

## Slide 43: Three-Chip (3-CCD / 3-CMOS) Colour Cameras
Incoming light passes through a dichroic prism.
Light is split into:
  Red → Sensor 1
  Green → Sensor 2
  Blue → Sensor 3
Each sensor captures full resolution for its colour.

## Slide 44: CMOS
Key Characteristics
Excellent color accuracy
High resolution
No demosaicing artifacts
Superior image quality
Bulky
Expensive
Precise optical alignment needed
Applications
Broadcast cameras
Cinematography
High-end industrial inspection
Scientific imaging

## Slide 45: Camera Performance Parameters - Noises